|  | ......................... pc € .............................. € .............................. GEZE SecuLogic System TZ 320 Comfort for securing a door along escape and rescue routes with electric lock in accordance with EltVTR. Suitable for connection to swing door drives, motor locks, fire alarm systems, burglar alarm systems as well as relaying messages to the building management system and much more. Extension of the functionality of the door control unit TZ 320 S by another 4 inputs and 6 outputs. System comprises: |
| --- | --- |
|  | ......................... pc € .............................. € .............................. GEZE SecuLogic TZ 320 BS door control unit in bus technology With integrated control unit, illuminated emergency button indication sign and key switch. Tested in accordance with EltVTR. Equipped with: • Control unit with illuminated emergency button LED displays for the operating status: Door locked / unlocked / unlocked for short time Door open / closed Alarm, pre-alarm, malfunction Coloured terminals to differentiate the connections for the periphery. Large-surface barrier-free impact cover with sabotage protection. Integrated weekly timer as well as automatic storage of the operating mode and the user data after power failures of up to 24 h. 3 programmable inputs, 2 programmable outputs • Integrated, illuminated emergency buttons indication sign • Key switch with 2 switch contacts, incl. profile half cylinder to adjust the short-time release, permanent unlocking, locking functions and to reset the alarm Operating voltage 24 V DC Connections: • 3 programmable inputs to connect timer, fire alarm system, burglar alarm system, access control, locks with cylinder contact and much more. Function: high active, low active and deactivated, can be selected for each status • 2 programmable outputs to connect swing door drive, motor lock, lever lock, additional electric strike, optical or acoustic alarm indication and much more. Function: normally opened contact, normally closed contact and deactivated can be selected for each status • Input for indirect release via external emergency buttons • Input for external key switch to control the operating modes • Input for feedback of the door status • Input for feedback of the locking status • Prepared for networking via GEZE BUS with visualisation software VAT 220 SN, control panel TE 220/TTE 220 and OPC interface OPC 220 Functions: • Termination and retriggering in conjunction with short-time unlocking • Combination with GEZE swing door drives possible without additional components • Control and visualisation via visualisation software VAT 220 S N and control panel TE 220/TTE 220 plus transmission to BMS via OPC interface possible. Burglar alarm system, fire alarm system signals as well as the timer can be passed on via the GEZE BUS to all participants in a bus line. 5 groups possible on each line. • Integrated security interlocking door function (active, passive and combined). 10 groups possible. • Relaying of system status to BMS via potential-free outputs • Relaying of collective messages such as door status, alarm and locked to BMS • Integrated buzzer for acoustic signalling of alarms and pre-alarms • Integrated weekly timer • Alarm memory with date and time • Automatic storage of operating status and user data following power failures up to 24 h. Version: ( ) Surface mounting: Dimensions (W x H x D): 77 x 197 x 90 mm ( ) plastic housing in colour similar to RAL 6032 (green) ( ) plastic housing in colour white aluminium ( ) Flush mounting: Dimensions (W x H x D): triple frame 81 x 152 x 62.5 mm ( ) switch range AS500 by Jung in alpine white ( ) switch range LS990 by Jung in stainless steel ( ) switch range E2 by Gira in white ( ) switch range E2 by Gira in anthracite Other switch ranges in System 55, e.g. Berker B1, B3, S1, Merten System M, Feller, Gira E22, Event are possible. Use for doors: ( ) single-leaf ( ) double-leaf |
|  | ......................... pc € .............................. € .............................. GEZE SecuLogic TZ 320 S door control unit in bus technology With integrated control unit, key switch and emergency button indication sign. Tested in accordance with EltVTR. Equipped with: • Control unit with illuminated emergency button LED displays for the operating status: Door locked / unlocked / unlocked for short time Door open / closed Alarm, pre-alarm, malfunction Coloured terminals to differentiate the connections for the periphery. Large-surface barrier-free impact cover with sabotage protection. Integrated weekly timer as well as automatic storage of the operating mode and the user data after power failures of up to 24 h. 3 programmable inputs, 2 programmable outputs • Integrated emergency buttons indication sign, unlit • Key switch with 2 switch contacts, incl. profile half cylinder to adjust the short-time release, permanent unlocking, locking functions and to reset the alarm Operating voltage 24 V DC Connections: • 3 programmable inputs to connect timer, fire alarm system, burglar alarm system, access control, locks with cylinder contact and much more. Function: high active, low active and deactivated, can be selected for each status • 2 programmable outputs to connect swing door drive, motor lock, lever lock, additional electric strike, optical or acoustic alarm indication and much more. Function: normally opened contact, normally closed contact and deactivated can be selected for each status • Input for indirect release via external emergency buttons • Input for external key switch to control the operating modes • Input for feedback of the door status • Input for feedback of the locking status • Prepared for networking via GEZE BUS with visualisation software VAT 220 SN, control panel TE 220/TTE 220 and OPC interface OPC 220 Functions: • Termination and retriggering in conjunction with short-time unlocking • Combination with GEZE swing door drives possible without additional components • Control and visualisation via visualisation software VAT 220 S N and control panel TE 220/TTE 220 plus transmission to BMS via OPC interface possible. Burglar alarm system, fire alarm system signals as well as the timer can be passed on via the GEZE BUS to all participants in a bus line. 5 groups possible on each line. • Integrated security interlocking door function (active, passive and combined). 10 groups possible. • Relaying of system status to BMS via potential-free outputs • Relaying of collective messages such as door status, alarm and locked to BMS • Integrated buzzer for acoustic signalling of alarms and pre-alarms • Integrated weekly timer • Alarm memory with date and time • Automatic storage of operating status and user data following power failures up to 24 h. Version: ( ) Surface mounting: Dimensions (W x H x D): 77 x 197 x 90 mm ( ) plastic housing in colour similar to RAL 6032 (green) ( ) plastic housing in colour white aluminium ( ) Flush mounting: Dimensions (W x H x D): double frame 81 x 152 x 62.5 mm ( ) switch range AS500 by Jung in alpine white ( ) switch range LS990 by Jung in stainless steel ( ) switch range E2 by Gira in white ( ) switch range E2 by Gira in anthracite Other switch ranges in System 55, e.g. Berker B1, B3, S1, Merten System M, Feller, Gira E22, Event are possible. Use for doors: ( ) single-leaf ( ) double-leaf |
|  | ......................... pc € .............................. € .............................. Terminal box KL 220 To extend the functionality of the door control unit TZ 32x by another 4 inputs and 6 outputs. Connection via internal 2-wire interfaces to the door control unit. Connections: • 4 programmable inputs to connect timer, fire alarm system, burglar alarm system, access control, locks with cylinder contact and much more. Function: high active, low active and deactivated can be selected for each status • 6 programmable outputs to connect swing door drive, motor lock, lever lock, additional electric strike, visual or acoustic alarm indication and much more. Function: normally closed contact, normally opened contact, and deactivated can be selected for each status Dimensions (WxHxD): ( ) Surface mounting: 113 x 113 x 58 mm ( ) Flush mounting: 107 x 107 x 57 mm ( ) integrated in swing door drive KL 220/TSA 160 Technical data: Power supply Supply voltage 230 V AC Operating voltage 24 V DC Output power max. 600 mA for periphery |
|  | ......................... pcs. .............................. € .............................. € GEZE escape door lock FTV 320 Electric lock for doors along escape and rescue routes according to the closed-circuit principle. Guarantees reliable and immediate unlocking of the door, even with high latch preload. With integrated feedback contact for monitoring the door mode and locking state as well as for sabotage monitoring. High resistance against attempts to break open. Universal use: DIN right / left hand, horizontal / vertical, door leaf / frame. Face plate pre-assembled to locking element, strike plate can be ordered separately as counterpart. Operating voltage: 24 V DC Current consumption: 100 mA in locked state Current consumption: 240 mA briefly during locking Operating temperature: -20 / +60 °C Suitability certificate: EltVTR Break-open resistance: at least 5,000 N Latch preload: at least 3,000 N Clearance: 5 mm ± 2 mm Dimensions: 15.2 x 138.8 x 37.7 mm (W x H x D) Note: The escape door lock is mounted in addition to the existing panic lock. Face plate version (W x H x D): ( ) Flat face plate 20 x 200 x 3 mm round ( ) Flat face plate 22 x 220 x 3 mm, rectangular ( ) Flat face plate 24 x 200 x 3 mm rectangular ( ) Flat face plate 24 x 200 x 3 mm round ( ) Flat face plate 25 x 200 x 3 mm rectangular (replacement for FTÖ 331) ( ) Flat face plate 28 x 200 x 3 mm, rectangular ( ) Flat face plate 30 x 200 x 3 mm, rectangular ( ) Angled face plate 30 x 48 x 220 x 3 mm, rectangular (replacement for FTÖ 331) ( ) Face plate with latch guide 35 x 200 x 3 mm, rectangular (replacement for FTÖ 331) Strike plate escape door lock FTV 320 As counterpart to the escape door lock, made of corrosion-resistant stainless steel. Version (W x H x D): ( ) Flat strike plate 20 x 110 x 3 mm, rectangular ( ) Flat strike plate 20 x 110 x 3 mm, round ( ) Flat strike plate 20 x 140 x 3 mm, round ( ) Flat strike plate 22 x 220 x 3 mm, rectangular ( ) Flat strike plate 24 x 110 x 3 mm, rectangular ( ) Flat strike plate 24 x 110 x 3 mm, round ( ) Flat strike plate 24 x 130 x 3 mm rectangular ( ) Flat strike plate 24 x 140 x 3 mm rectangular ( ) Flat strike plate 24 x 140 x 3 mm round ( ) Flat strike plate 28 x 130 x 3 mm, rectangular ( ) Flat strike plate 28 x 140 x 3 mm, rectangular ( ) Flat strike plate 30 x 140 x 3 mm, rectangular ( ) Flanged strike plate, can be shortened, 20 x 140 x 3 mm round ( ) Flanged strike plate, can be shortened, 24 x 140 x 3 mm rectangular ( ) Flanged strike plate, can be shortened, 24 x 140 x 3 mm round ( ) Flanged strike plate, can be adjusted and shortened 20 x 140 x 4 mm, round ( ) Flanged strike plate, can be adjusted and shortened 24 x 140 x 4 mm, rectangular ( ) Flanged strike plate, can be adjusted and shortened 24 x 140 x 4 mm, round Support for strike plate escape door lock FTV 320 For compensating clearance exceeding 6 mm between the face plate and the strike plate. One support required for clearance between 6 – 9 mm. Two supports required for clearance between 9 – 12 mm. When clearance between face plate and strike plate is greater than 8 mm, no recess is required for the strike plate. The cross latches catch in the supports which are fitted under the strike plate. Version (W x H x D): ( ) Support strike plate 20 x 140 x 1 mm, rectangular ( ) Support strike plate 24 x 140 x 1 mm, rectangular ( ) Support strike plate 24 x 140 x 3 mm, rectangular ( ) Support strike plate 28 x 140 x 1 mm, rectangular ( ) Support strike plate 28 x 140 x 3 mm, rectangular As an option, a support can be fitted under the face plate rather than under the strike plate. ( ) Support face plate 24 x 200 x 1 mm, rectangular ( ) Support face plate 24 x 200 x 3 mm, rectangular |
|  | ......................... pc € .............................. € .............................. GEZE holding magnet MA 500 with counterplate for magnetic locking of escape doors. Pressure resistance against attempted burglary 5000 N, with integrated Hall sensor for monitoring and bicolour LED to display the door mode. Rated voltage 24 V DC, PG9 connection, Current consumption 250 mA, Version: silver-coloured Installation with one installation set only: ( ) on the hinge side ( ) on the opposite hinge side ( ) as frame installation with reed contact: ( ) flat reed contact with bracket ( ) flat reed contact with cross hole and base ( ) block reed contact with base for steel doors Note: The holding magnet is normally installed in addition and away from the existing panic lock. |
|  | ......................... pc € .............................. € .............................. Planning costs Costs for producing cable diagrams and connection diagrams for individual projects and the preparation of functional descriptions. |
|  | ......................... pc € .............................. € .............................. Installation, start-up and official approval Installation, start-up and official approval of the system described with instruction. |
|  | ......................... pc € .............................. € .............................. Emergency exit system maintenance service package - compact (standard) Service package for maintenance in accordance with EltVTR as well as according to manufacturer’s specifications with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - response time of 24 hours after the fault was reported on workdays (Monday - Friday, 7 am – 5 pm) - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years. |
|  | ......................... pc € .............................. € .............................. Emergency exit system maintenance service package - comfort (optional position) Service package for maintenance in accordance with EltVTR as well as according to manufacturer’s specifications with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to € 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years. |